## Slide 1: Storing Forage in Silage Piles
Jerry Clark
UW Extension Educator
Chippewa County
Dr. Brian Holmes
UW-Extension
Dept. Biological Systems
Engineering

## Slide 2: Silage Piles-advantages
Short or long term storage
Inexpensive
Filling through Feedout Dry Matter Losses Less Than 21% with Good Management

## Slide 3: Silage Piles-disadvantages
Dry matter losses greater than 50% without proper management
Space requirements
Possible distance from feeding area

## Slide 4: Siting
Need all weather access
Best is concrete or asphalt slab
Macadam surface can work
Bare ground or macadam may lead to feed contamination
Macadam Drive

## Slide 5: Siting
2% slope to allow rainfall and seep drainage
More than one pile
  May form feeding center

## Slide 6
60
100-
120
100-
120
260-
300
N
Commodity
Shed
Commodity
Bins
Silage Piles – Long Term Feed Center Plan
Dispose of
Drainage Properly

## Slide 7
60
100-
120
N
Commodity
Shed
Commodity
Bins
Silage Piles – Phase I
Dispose of
Drainage Properly

## Slide 8
60
100-
120
100-
120
260-
300
N
Commodity
Shed
Commodity
Bins
Silage Piles – Phase II
Dispose of
Drainage Properly

## Slide 9
60
100-
120
100-
120
260-
300
N
Commodity
Shed
Commodity
Bins
Silage Piles – Long Term Feed Center Plan
Dispose of
Drainage Properly

## Slide 10: Siting -Wells
Locate > 100 feet from well
Down slope from wells
Lighter soils – distance may be greater
Collect leachate and dispose properly
Effect of Seepage
Tank Inlet
Settled Solids
Screen

## Slide 11: Filling
3/8" to 3/4" theoretical length of cut
Better fermentation if cut short
Whole plant moisture
  65-70% corn silage
  60-65% hay silage
Bastiman 1976

## Slide 12: Filling
Progressive wedge technique
6” layer maximum
Side slope of 3:1 (horizontal:vertical)
Triangle cross section for small piles
Trapezoid cross section for larger piles
Pile height limited by reach of unloading equipment
Needs Shallower
Side Slopes

## Slide 13: Packing
Pack! Pack! And Pack some more!!!

## Slide 14
GO PACK!

## Slide 15: Packing
Packing Tractor
  Shuttle shift
  Roll over protection & seat belts
  As heavy as possible
  Duals add safety not necessarily better packing

## Slide 16: Packing
Packing time
_ Multiple passes/multiple directions
  5 minutes per ton of wet forage
  ½ hour before and after filling

## Slide 17
Max. Packing Time – One Tractor

## Slide 20: Covering
Cover as soon as possible
6 mil plastic
Tires touching each other
Seal edges
Needs More
Tires

## Slide 21: Feedout
Minimum 12 inches removal per day-minimizes spoilage
Keep Smooth Face –Consider Facer
Less can be fed out during winter

## Slide 22
360 ft - one year
or
180 ft
180 ft
120 ft
120 ft
120 ft
or
Example:
  360 day feed storage period
  Total Length of pile(s) should be 360 feet long, consider several piles
Feedout

## Slide 23: Summary
Inexpensive way to store forage
Direct expenses include pad, labor, packing & unloading equipment, plastic, fuel
Indirect expense is forage dry matter loss
$

## Slide 24: Tips for Success
Harvest at correct moisture
Proper siting and construction
Thorough packing
Immediate covering
Proper feedout